## Slide 1: Unit 5
Electric Braking

## Slide 2
Braking is the process to reduce the speed of
any moving or rotating equipment

## Slide 3: Types of braking
Mechanical braking
Electric braking

## Slide 4: Electric braking
In electric braking, the braking energy is converted into
electric energy instead of converting it into heat energy
at the brake shoes (as in mechanical braking) and either
Dissipated in the resistances or returned to the supply.

## Slide 5: Types of electric braking
Plugging or reverse current braking
Rheostatic or dynamic braking
Regenerative braking

## Slide 6: Plugging or reverse current braking
Simplest method of electric braking
In this method the torque of the motor is reversed by reversing the supply connection.
It makes the motor and the driven machine to standstill condition.
A special device is required to cut off the supply as soon as motor comes to rest.
Better braking torque than rheostatic braking.

## Slide 7: Rheostatic or dynamic braking
In this method of braking the motor is disconnected from the supply and operated as a generator driven by the kinetic energy of the rotating parts of the motor and its driven machines.
Thus the kinetic energy of rotation is converted into electrical energy, which is dissipated in the external resistance connected across the motor at the braking instant.
The advantage of this method is that no energy is required from the supply to brake the motor.

## Slide 8: Regenerative braking
In this method the motor is not disconnected from the supply.
It remains connected to it and feeds back the braking energy or kinetic energy to the system.
As no energy is wasted in this method and it is supplied back to the system thus overall energy is saved. Hence it is better than plugging and rheostatic braking.
Mostly used when the load on the motor has overhauling characteristic as in the lowering of hoist or downward motion of an electric train.

## Slide 9: Regenerative braking for dc shunt motor
This type of braking in dc shunt motor is possible when the overhauling load acts as a prime mover and so drives the machine as a generator.
In this case back emf is greater than supply voltage
Consequently direction of armature current and hence armature torque is reversed because of which speed falls until back emf becomes less than supply voltage.
Then after motoring mode starts.
To stop the machine at the point when back emf is equal to supply voltage we have to cut off the supply line.
Mechanical brakes required in order to hold the motor at standstill condition.
All the dc shunt motors are provided with regeneration capability